## Slide 1
Problem Statement
To develop an IoT-based smart system for real-time monitoring of water level and quality, along with leakage detection, to minimize water wastage and improve efficient water management.
Team Name
FORASDANGA REVOLUTION

## Slide 2
Problem Identification & Analysis
1. Understand the Problem:
  Real-World Problem: Massive water wastage caused by unmonitored tank overflows, undetected pipeline leaks, and consumption of contaminated water due to lack of real-time monitoring.
  Who Faces It & Where: Homeowners, housing societies, educational campuses, and commercial facilities.
  Existing Solutions: Traditional mechanical float valves and manual visual checks.
  Gaps & Limitations: Mechanical valves frequently fail, lack real-time alerts, cannot detect silent pipe leaks, and provide zero insights into water purity.
2. State the Problem:
Identified problem: “Unmonitored water tanks and distribution pipes lead to significant water wastage through silent leaks and overflows, alongside unmonitored water quality that poses health risks.”
3. Describe Your Solution:
“We propose to develop an IoT-based Smart Water Management System that will monitor water levels, detect contamination, and identify pipeline leakages in real-time with automated shut-off feature.”

## Slide 3
Proposed Technical Approach
Working Flow:
Data Input: The HC-SR04 ultrasonic sensor transmits high-frequency sound waves through its trigger pin and clocks the travel time of the reflected echo pulse to read the distance to the water surface. Concurrently, the potentiometer supplies an analog voltage to simulate parameter thresholds or water quality input.
Main Processing (C++ Logic): The microcontroller reads digital pulse timings and analog signals, converting the pulse duration into centimeters using the relation Distance = (Time × 0.0343) / 2 .The algorithm averages readings to reject turbulence noise and maps the current level to capacity limits.
Threshold Comparison: The firmware compares the calculated water level against predefined boundary conditions (Low, Normal, Overflow/Leak).
Final Output & Action: The 16x2 LCD prints numeric distance and operating status in real time. Concurrently, digital output pins trigger the LEDs: Green for stable levels, Yellow for approaching limits, and Red for critical overflow or leak detection.

## Slide 4
Proposed Technical Approach
Working Flow:
https://youtu.be/Z6_uGqwxsyE?si=DPdjhsptEHMkqpfQ

## Slide 5
Technology Stack
1. Hardware:
HC-SR04 Ultrasonic Sensor: Used to continuously measure the water level in the tank without physical contact.
​16x2 LCD Display: Provides a local, real-time visual readout of the water level and system status.
​LEDs (x3): Act as visual indicators for different system states (e.g., Green for normal, Yellow for warning, Red for high-level alert/leakage).
​Potentiometers (x2): Used to adjust the contrast of the 16x2 LCD screen and to simulate variable sensor inputs (like water quality) during testing.
​Resistors: Essential passive components used to limit the current and protect the LEDs from burning out.
​Microcontroller (e.g., Arduino/ESP32): The main processing board used to read the sensor data and control the display and LEDs.!
2. Software:
Wokwi Simulator: A web-based electronics simulator used to design, build, and safely test the virtual circuit diagram before physical hardware assembly.
​C++ (Programming Language): Used to write the logic and firmware for the microcontroller, enabling it to calculate water distance, update the LCD, and trigger the LEDs based on specific thresholds.

## Slide 6
Feasibility & Viability
Technical Feasibility: Highly feasible using low-cost embedded hardware, standard C++ logic, and simple circuit design tested on Wokwi.
Resources Required: HC-SR04 ultrasonic sensor, 16x2 LCD display, 3 LEDs, 2 potentiometers, resistors, microcontroller board, and Wokwi IDE.
Budget: Approximately ₹1,000– ₹2,000 for physical prototyping components; ₹0 using Wokwi simulation.
Time: Yes, the simulation prototype is already implemented, and physical hardware assembly can be completed within 48 hours.
Challenge: Digital signal jitter and echo noise causing erratic readings.
Solution: Moving-average software filtering in C++ to discard outliers.
Future Scope: Integrate IoT cloud connectivity (ESP32/Blynk) for real-time mobile app alerts and add solenoid valves for automated emergency water supply cut-off.

## Slide 7
Target Beneficiaries: Households, housing societies, commercial buildings, and educational campuses requiring automated water management.
​Problem Solving & Efficiency: Eliminates tank overflows and hidden pipe leaks, reducing overall water wastage by up to 30–40%.
​Key Benefits & Safety: Provides real-time visual alerts (LCD/LEDs) to prevent property water damage and avoid manual inspection efforts.
​Impact Measurement: Effectiveness is measured by response time (< 2 seconds for sensor alerts) and total liters of water conserved daily.
​Limitations & Future Scope: Currently dependent on local hardware connections; future iterations will add IoT cloud logging and solar power.
Impact & Benefits

## Slide 8
THANK YOU
Ultrasonic Water Level Indicator & Monitoring System